## Slide 1
Lecture 3:
Parallel Computing Fundamentals,
Amdahl, Base Core Equivalents & UML
Presented by
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
Planned to be double period lecture

## Slide 2: Lecture Overview
Review of quiz 0
UML blurb
Parallel computing fundamentals
Amdahl’s Law
Base Core Equivalents (BCEs)
Calculating performance using BCEs

## Slide 3
Quiz 0 Review…
37 students wrote the quiz

## Slide 4: Quiz0 review: Q1
Q1 How good is your VHDL
Chart: How good is your VHDL?
| None | A little | Reasonably good | Excellent
 | 2 | 2 | 22 | 4
None | 7%
A little | 7%
Reasonably good | 73%
Excellent | 13%
 | 100%

## Slide 5: Quiz0 review: Q2
Q3 What is Xilinx ISE?
[1] No idea - I would probably delete it from my PC if I found it there
[2] It is a software tool for analyzing Inter-Species Expressions (like the face your dog makes when he sees your neighbor's cat and then barks like mad).
[3] It is an application for converting C code into BASIC
[4] It is an application used to develop HDL code and programme FPGAs
[1] | 47%
[2] | 0%
[3] | 0%
[4] | 53%
 | 100%
% breakdown of answers

## Slide 6: Quiz0 review: Q3
Q2 The 'Internet of Things' has become a catchy term. Explain briefly what this refers to.
0/3: but thanks for the honesty!... so 100 brownie points for you 
1/3: Not really about what the internet has become & offloading computing
2/3 maybe more: This is more correct, but isn’t everything (and neither limited to households items as some people said.) (Getting the geyser to check the weather sounds like an interesting research project!!)
…. maybe +1 for novelty, at least 1,000 brownie points for you
My thoughts…

## Slide 7: Quiz0 review: Q3
Q2 The 'Internet of Things' has become a catchy term. Explain briefly what this refers to.
The 'internet of things' (IoT) refers to a larger scale internet in which everyday objects, like alarm clocks, light bulbs and such like, are connected to a network that allows data to be sent to or received from them.
Sample solution
Yebo! It is 100% right.
Mark? …
3/3
(that’s sometimes the problem with marking your own work)
+100 brownie points for good grammar 
+1 bonus mark for fun

## Slide 8: Quiz0 review: Q4
Q4 Motivate why computer engineers, planning to work on large and complex FPGA projects, should understand both Verilog and VHDL.
Nice story but didn’t quite interpret the question as planned (in reflection an imperfectly phrased question). 2/3 ?
Bit too much intro, didn’t take it quite far enough 2/3
Ag shame! Missed the mark. 0/3
My thoughts…

## Slide 9: Quiz0 review: Q4
Q4 Motivate why computer engineers, planning to work on large and complex FPGA projects, should understand both Verilog and VHDL.
Answer:
The main reason is reuse. Reusing existing gateware devices. For example, there might be an excellent digital filter out there on the web (e.g. opencores) that does almost what you want; but it’s in Verilog instead of your favorite VHDL. So you have to either start from scratch or learn Verilog.
Now you’re talking
big savings & benefits
3/3

## Slide 10: Quiz0 review: Q5
Q3 What is spatial computing?
[1] A new programming language
[2] A programming paradigm whereby computation is described as happening in different spaces instead of different times.
[3] This term (if rather informal) refers to an algorithm implementation that has certain awkward imperfections; kind of like when someone accidentally snorts uproariously at a good joke in polite company.
[4] It refers to fitting computing infrastructure into a limited space.
How did the class respond?...
Nice try,
wise-guy!
X for office use=
Most of the class got it right though!
A technically wrong response:

## Slide 11: Quiz0 review: Q6
Why would the concept of an embedded system possibly be mixed with the notion of a high performance computer? Surely an embedded system is something you would find in commonplace gizmos, like the alarm clock that you bash in the face or wack om the head each day. Explain this bazar turn of events, perhaps making reference to a definition of an embedded system.
My thoughts…
My thoughts on the topic: some high performance computers are becoming highly task-specific – the trend is moving away from supercomputers for general applications, towards platforms that are more custom-designed (or tailored) to a particular domain of application (or even to a specific application – e.g., reconfigurable computing platforms).
2/4 A good start to the story... But then the author laments the possible lack of HPC games (would you really miss MineSweeper so much?).
1/4 So close, but didn’t mention HPCs!! (so 1 for effort)

## Slide 12: Quiz0 review: Q6 – elaboration
Good: |  |  |  | 
HPC system can be in the form of an embedded system: its special purpose, must be fast, real-time, and perform tasks concurrently. |  |  |  | 
An HPC with a well defined task can be optimised for that task - hence akin to an embedded system. |  |  |  | 
Bad: |  |  |  | 
An embedded system can be very complex, such as a HPC placed into a bigger system, still making it embedded. |  |  |  | 
HPCs are trending towards embedded systems because they are becoming more task specific. |  |  |  | 
To enhance performance and increase functionality (?) |  |  |  | 

## Slide 13: Quiz0 review: Q7
Q: In computer engineering terminology, what does 'co-design' mean?
0/5 Not right
0/5 Walk like an Egyptian? Nice idea, but I’ll try to resist that.
A: co-design means:
Software/Hardware co-design is generally considered simultaneous design of both hardware and software to implement required functions. Often it refers to a hardware team and a software team needing to work closely together while developing the software and hardware parts of an embedded system, together with the activities involved in acheiving this, such as defining clear hardware/software interfaces, functional decomposition, etc.

## Slide 14: Quiz0 review: Q8
1/1 Spot on!
If we considered that 000000012 was 12810 would we be considered as little-endians or big-endians?
Mainly in this course we’ll be little-endians… it tends to be much more common and natural in terms of writing and theorizing.

## Slide 15
Some Answers from
Previous Quiz0’s
See extra slides at end of this presentation

## Slide 16
UML Review

## Slide 17: UML Review*
General errors that student often make:
  Not using the UML syntax (at all)
    Block and line models, things like flowcharts
  Using the UML syntax wrongly
    Invalid modelling constructs (i.e., wrong type of connectors / associations and blocks)
    Vague models
    Insufficient information
Some examples of common mistakes…
* No longer is UML assessment in Quiz0 due to time constraints

## Slide 18: UML demonstration
JOE'S STORY: Joe Baggits is a developer in the Construction Division of Freezit Commerial Products (FCP) Pty. Ltd. The FCP corporation produces a variety of Cooling systems, grouped into two product ranges, namely: 1) the portafrige range and 2) the coolzone range. The portafrige range includes the Icecart™ and the Chillblock™. Coolzone range includes the ShopFrige™ and Coolroom™. Andy Wrapp is also a developer in the Construction Division and is Joe's manager. Joe works on portafridge products, whereas Andy works on coolzone products.
Task: Produce a UML model describing the products and people related to Joe Baggits, according to the description below.
Look at this if your UML understanding is lacking.

## Slide 19
Sample
Solution
Notice use of roles, aggregation and inheritance.
In this situation, it is handy to use objects instead of classes to clearly capture things that exist as physical entities (e.g., the people)

## Slide 20
Containment
Aggregation
vs.
Container
Group
Item in the container
Item in the group
Container has solid diamond
n
1..*
Aggregation has outline diamond
Arity next to item
(not next to container)
Key to arity: n  exactly n. 1..*  1 or more * = zero or more

## Slide 21: Super fast class exercise
(for Thurs double)
Briefly describe the following as a UML diagram:
A new computer system called PMB (Parallel Multicore Beast) contains eight CPUs and two blocks of 8Gb memory. It can run multiple programs from its built-in Linux O/S. Each program can spawn multiple threads. The programs each contain one or more data blocks.
Take around 5 minutes to draw a rough UML class diagram
If you haven’t used UML don’t worry, just used the containment and aggregation links shown earlier.

## Slide 22: Sample solution
A new computer system called PMB (Parallel Multicore Beast) contains eight CPUs and two blocks of 8Gb memory. It can run multiple programs from its built-in Linux O/S. Each program can spawn multiple threads. The programs each contain one or more data blocks.
PMB
8GB Memory
2
8
CPU
Thread
1..*
Assumptions:
Threads are contained in a program, and there must be at least one thread in a program.
By stating Linux is built-in it indicates that this O/S is an instrumental non-optional aspect so this is probably more a containment relation than an aggregation.
Data block
1..*
*
Linux
Program

## Slide 23: Parallel Systems
EEE4084F: Digital Systems
A?
B?
C?
+
*
X !
Y !
-

## Slide 24
Anyone else beside me feel that way?
…
Question:
Do you sometimes feel that despite
having a wizbang multicore PC,
it still just isn’t keeping up well
with the latest software demands?...
Processor cores
Major software

## Slide 25
It may be so because your software isn’t designed to leverage the full potential of the available hardware.
CPUs at idle

## Slide 26: Computation Methods
Hardware
Reconfigurable
Computer
Software
Processor
e.g. PCBs, ASICs
Advantages:
High speed & performance
Efficient (possibly lower power than idle processors)
Parallelizable
Drawbacks:
Expensive
Static (cannot change)
e.g. IBM Blade, FPGA-based
computing platform
Advantages:
Faster than software alone
More flexible than software
More flexible than hardware
Parallelizable
Drawbacks:
Expensive
Complex
(both s/w
& h/w)
e.g. PC, embedded software on microcontroller
Advantages:
Flexible
Adaptable
Can be much cheaper
Drawbacks:
The hardware is static
Limit of clock speed
Sequential
processing

## Slide 27
Short Video:
Latest Intel Chipsets
Intel's New 4th Gen Core i7 Processors and More - PAX Prime 2014.mp4
https://www.youtube.com/watch?v=Q8Akad-OxRI

## Slide 28: Quick view: Intel’s Latest CPUs
Intel® Core™ i7
  I7 Extreme Edition vs. (regular) i7 processor
Intel® Xeon™ Processors
  4/8 cores; 8/16 threads; 40W to 130W (more cores, exponential growth in power)
  1.86-3.3 Ghz CPU clock, 1066-1600 Mhz bus
Intel® Itanium®
  Scalable. 1/2/4 cores; hyperthreading*
  Allows designs up to 512 cores, 32/64bit
  Power use starts around 75W
  1-2.53 Ghz (Itanium 9500 ‘Poulson’); QPI 6.4GT/s bus
* Hyperthreading  two virtual/logical processors per core (more: http://www.techopedia.com/definition/2866/hyperthreading-ht)
gigatransfers per second (GT/s) or megatransfers per second (MT/s): (somewhat informal) number of operations transferring data that occurs each second in a given data-transfer channel. Also known as sample rate, i.e. num data samples captured per second, each sample normally occurring at the clock edge. [1]

## Slide 29
Intermission

## Slide 30: Mainstream parallel computing
Most server class machines today are:
  PC class SMP’s (Symmetric Multi-Processors *)
  2, 4, 8 processors - cheap
  Run Windows & Linux
Delux SMP’s
  8 to 64 processors
  Expensive:
  16-way SMP costs ≈ 4 x 4-way SMPs
Applications: Databases, web servers, internet commerce / OLTP (online transaction processing)
Newer applications: technical computing, threat analysis, credit card fraud...
SMP offers all processors and memory on a common front side bus (FSB –bus that connects the CPU and motherboard subsystems).
* Also termed “Shared Memory Processor”

## Slide 31: Large scale parallel computing systems
Hundreds of processors, typically built as clusters of SMPs
Often custom built with government funding (costly! 10 to 100 million USD)
  National / international resource
  Total sales tiny fraction of PC server sales
Few independent software developers
Programmed by small set of majorly smart people

## Slide 32: Large scale parallel computing systems
Some application examples
  Code breaking (CIA, FBI)
  Weather and climate modeling / prediction
  Pharmaceutical – drug simulation, DNA modeling and drug design
  Scientific research (e.g., astronomy, SETI)
  Defense and weapons development
Large-scale parallel systems are often used for modelling

## Slide 33: Amdahl’s Law
EEE4084F
Speed-up
Number of processors

## Slide 34: Amdahl’s Law: History
The guy: Gene Amdahl
  Was chief architect for IBM's first mainframe series of computers
  Founder of Amdahl Corporation
Amdahl found stringent restrictions on the speedup possible for given parallelized tasks.
Thee observations packaged as: Amdahl's Law

## Slide 35
Video Clip…
Linux Magazine Video: Understanding Parallel Computing: Amdahl's Law
Amdahl.flv
https://www.youtube.com/watch?v=WdRiZEwBhsM

## Slide 36: Amdahl’s Law
Define f as: fraction of computation that can be parallelized (ignoring scheduling overhead)
Then (1 - f ) is the fraction that is sequential
Define n = no. processors for parallel case
The maximum speed-up achievable is:
1
f
( 1 – f ) +
n
Speedupparallel =
Classic version
Should be able to remember this formula for exams

## Slide 37: Amdahl’s Law: Alternate Representation
P = expected performance improvement
Eu = Execution time on a uniprocessor (serial)
Ep = Execution time on a number of processors (parallel)
n = number of processors
S = fraction of time spent in the sequential time

## Slide 38: Homework task
Watch 2nd part of Amdahl’s law video
Amdahl2.flv
Understanding Parallel Computing (Part 2): The Lawn Mower Law
LinuxMagazine

## Slide 39: Designing Multicore Chips
Designers contend with single-core design options
  Wakeup (of sleeping cores), Instruction fetch, Instruction Decoding
  Variable clock speeds (e.g. power saving modes)
  Execution unit
  Execution modes (e.g. system, user, interrupt)
  Load/queue(s) & data cache
As well as additional design degrees of freedom for parallel architectures
  How many cores? Size & features of each?
  Shared caches? Cache levels?
  Memory interfacing? How many memory banks? Where to place them?
  On-chip interconnects: bus structures, switching fabric, ordering and priority of cores/devices?

## Slide 40: BCE Abstraction
It all gets a bit complicated to keep track of, therefore to theorize and predict performance expectations, the concept of a Base Core Equivalent was proposed…

## Slide 41: Base Core Equivalent (BCE)
EEE4084F

## Slide 42: Calculating performance using BCEs
A great many papers on the subject of Amdahl’s law
Many mention the term BCE
BCE = Base Core Equivalent
  A single processing core in a multicore processor design

## Slide 43: BCE: Simple Multicore Hardware Model
An abstracted hardware model to complement Amdahl’s software model
The simplified model…
Chip Hardware, abstracted as
  Multiple Cores (with L1 caches)
  Supporting architecture (L2/L3 cache banks, interconnect, pads, etc.)
Resources for Multiple Cores Bounded
  Due to area, power, cost, or multiple factors…
  Bound of N resources per chip for cores
  Bound in terms of Power and Area

## Slide 44: 1x BCE vs. 1x N-BCE vs. Mx N-BCE
Remember that the BCE is equivalent to a basic single core processor
= 1x 1-BCE
= 16x 1-BCE
= 16x 4-BCE
It’s an abstraction, and likely not very precise. For example a 16x4-BCE may have faster comms between cores in same block and slower comms between cores in different blocks, whereas the 16x1-BCE might have the same speed comms between all cores.

## Slide 45: Example processor structures Symmetric vs. Asymmetric multicores
Symmetric multicore 16 one-BCE cores
Symmetric multicore 4 x 4-BCE megacores
Asymmetric multicore comprising 2 x 4-BCE cores + 8 x 1-BCE cores
Clearly can become increasingly more difficult to achieve very accurate equivalences due to the architecture structures and things like memory latencies and inter-core comms.
a BCE
core
with 4-BCE
(I call them megacores to emphasize it equates to multiple BCEs)

## Slide 46: Symmetric core model
Variables:
n cores per chip
each core consumes r BCEs
16 x 1-BCE
n = 16, r=1
perf(r) = performance (speedup) of r-BCE over 1-BCE
Always perf(r) <= r (i.e. diminishing returns on increased parallelism)
Good heuristic: perf(r)=sqrt(r)
Symmetric four 4-BCE megacores

## Slide 47: Modelling Performance of Symmetric Multicore Chips
n cores per chip
r BCEs per megacore
Parallel Fraction of execution is F
Assume symmetric  all cores identical
Serial Fraction is 1-F and uses 1 megacore at rate perf(r)
Therefore: Serial time = (1 – F) / perf(r)
Parallel Fraction uses n/r megacores at rate perf(r) each
Parallel time = F / (perf(r) * (n/r)) = F*r / perf(r)*n
Therefore, w.r.t. one base core:
Implications?..
Symmetric Speedup =
1
+
1 - F
perf(r)
F * R
perf(r)*n
Enhanced Cores speed Serial & Parallel
Serial Fraction
1-F
Parallel
Fraction F
Execution Time

## Slide 48: Calculate performance…
Parallel fraction F=90%
Parallel fraction F=50%
Model up to 50 BCEs
Speedup 
r 
BCEs/megacore

## Slide 49: Asymmetric (Heterogeneous) Multicore Chips
Symmetric Multicore required all cores equal
Let’s enhance some (not all) of the cores in the processor chip…
For Amdahl’s simplified assumptions
  One Enhanced Core
  Others are base cores
How does this effect our hardware model?

## Slide 50: Asymmetric Multicore Chips
Chip bounded to total of n BCEs
One r-BCE megacore leaves n -r BCEs
Asymmetric case: one r-BCE megacore with n - r BCEs (i.e. one 4-BCE and 12 1-BCEs, r=4, n=16)
Symmetric case: four 4-BCE megacores (i.e. here r=4 and n=16)

## Slide 51: Modelling Performance of Asymmetric Multicore Chips
n cores per chip
1x r-BCEs , n-r 1-BCEs
Parallel Fraction of execution is F
Serial Fraction still 1-F and uses 1 core at rate perf(r)
Therefore: Serial time = (1 – F) / perf(r)
Parallel Fraction F uses 1 cores at rate perf(r) and n-r cores at rate 1
Parallel time = F / (perf(r) + n - r)
Therefore, w.r.t. one base core:
Implications?..
Serial Fraction
1-F
Parallel
Fraction F
Execution Time
Asymmetric Speedup =
1
+
1 - F
perf(r)
F
perf(r) + n - r

## Slide 52: Calculate performance…
Parallel fraction F=90%
Parallel fraction F=50%
Model up to r=64 BCEs
Speedup 
Parallel fraction F=99%
r 
BCEs/megacore

## Slide 53: Dynamic Multicore Chips
n base cores for best parallel performance
Harness r cores together for best serial performance (a bit of an optimistic dream perhaps)
Serial Case
1x n-BCE megacore
Parallel Case
n x 1-BCE cores

## Slide 54: Modelling Performance of Dynamic Multicore Chips
n base cores per chip where r can be harnessed
1x r-BCEs , n-r 1-BCEs
Parallel Fraction of execution is F
Serial Fraction 1-F uses r BCEs at rate perf(r)
Therefore: Serial time = (1 – F) / perf(r)
Parallel Fraction F uses n BCEs at rate 1 each
Parallel time = F / n
Therefore, w.r.t. one base core:
Implications?..
Serial Fraction
1-F
Parallel
Fraction F
Execution Time
Dynamic Speedup =
1
+
1 - F
Perf(R)
F
N

## Slide 55: Calculate performance…
Parallel fraction F=90%
Parallel fraction F=50%
Model up to r=64 BCEs
Speedup 
Parallel fraction F=99%
r 
BCEs/megacore
Looks wonderful! But it is realistic?

## Slide 56: BCE Performance Calculator – M Hill & M Marty
To apply Amdahl’s law to a multicore chip, we need
  A cost model for the number and performance of cores that the chip can support.
  1) assume a multicore chip can contain at most n base core equivalents (based on resources a chip designer devotes to cores & portion of code is parallelized)
  2) Assume (micro-)architects have techniques for using the resources of multiple BCEs to create a core with greater sequential performance.
    Let the performance of a single-BCE core be 1.
    Assume architects can expend the resources of r BCEs to create a more powerful processor with sequential performance perf(r).
    Example assume perf(r) = sqrt(r) … In other words, we assume efforts that devote r BCE resources will result in sequential performance r. Thus, architectures can double performance at a cost of four BCEs, triple it for nine BCEs, etc. Graph results…

## Slide 57: Amdahl’s Law Milticore Performance Calculator
Check out Hill and Marty’s Amdahl’s interactive grapher at:
http://research.cs.wisc.edu/multifacet/amdahl/
You can also download the OCTAVE / Matlab code to do these graphs!
Quiz example of
resultant graph…
How it works:
Specify #cores, portion parallel code, type of BCE cores to use

## Slide 58
Example run of Hill and Marty’s Amdahl’s interactive grapher:
Speedup 
r 
BCEs/megacore
Gives a comparison of the different architecture models. Clearly Dynamic is probably always going to win.

## Slide 59: Recommended Reading
Hill and Marty 2008: “Amdahl’s Law in the Multicore Era” Available: http://research.cs.wisc.edu/multifacet/papers/ieeecomputer08_amdahl_multicore.pdf
Good article on Wikipedia look over: http://en.wikipedia.org/wiki/Amdahl's_law
See Vula: L21 - 04563876 - Amdahl Law in the Multicore Era.pdf
NB: do try to read this one! *
* Questions on BCEs likely to to appear in test or exam

## Slide 60: Next lecture
Automatic parallelism
Moore’s law and related trends, from a high performance computing angle
Discussion of Prac2 & Pthreads
Conceptual Assignment planning
Finalizing Seminar Groups
Benchmarking, etc.

## Slide 61: Further Reading / Refs
http://unilearning.uow.edu.au/critical/1a.html
Some resources related to critical analysis and critical thinking:
http://www.deakin.edu.au/current-students/study-support/study-skills/handouts/critical-analysis.php
An easy introduction to critical analysis:
An online quiz and learning tool for understanding critical thinking:
Some resources related to systems thinking:
https://www.youtube.com/watch?v=lhbLNBqhQkc
https://www.youtube.com/watch?v=AP7hMdnNrH4
Suggestions for further reading, slides partially based / general principles elaborated in:
https://computing.llnl.gov/tutorials/parallel_comp/
http://www2.physics.uiowa.edu/~ghowes/teach/ihpc12/lec/ihpc12Lec_DesignHPC12.pdf

## Slide 62
Some Answers from
Previous Quiz0’s
(supplementary slides)

## Slide 63: Quiz0 review: Q1
How good is your VHDL? (tick answer)
[1] None [2] A little [3] Reasonably good [4] Excellent
Chart: 
| 1 - not used | 2 - A little | 3 - Reasonably | 4 - Excellent
Q1 | 0 | 17.2414 | 79.3103 | 3.4483
Excellent: 0%
Reasonably good
None: 0%
A little
2012
This year
2013
89%
11%

## Slide 64: Quiz0 review: Q3
Chart: Question 3: Quartus II Experience
| None | A Little | Reasonably Good | Excellent
 | 1 | 5 | 20 | 1
 | 1 | 5 | 20 | 1
Chart: 
| 1 - not used | 2 - A little | 3 - Reasonably | 4 - Excellent
Q3a - Use of QuartusII | 0 | 20.6897 | 75.8621 | 3.4483
2012
Chart: 
| 1 - not used | 2 - A little | 3 - Reasonably | 4 - Excellent
Q3b - Use of Xilinx | 86.2069 | 3.4483 | 10.3448 | 0
Have you used Altera Quartus II? Or Xilinx ISE? Check appropriate boxes.
A little
A little
excellent
Reasonably good
(i.e. almost everyone has used it)
2013
Chart: Question 3: Xilinx ISE Experience
| None | A Little | Reasonably Good | Excellent
 | 23 | 1
Not used
2013
2014

## Slide 65: Quiz0 review: Q4
Close! But no cigar 
My thoughts?...
More ‘intelligence’?!
My cellphone is probably as intelligent as my PC… as in not at all intelligent based on the turning test. Heading into troubled waters here

## Slide 66: Quiz0 review: Q4
Suggested sample answer…
I’d be happy with something clear & general. E.g.:
It is a computer that is able to perform multiple computations in parallel.
Pretty good, if a
bit wordy
Not precisely… That’s a special case

## Slide 67: Quiz0 review: Q6
A student’s answer…
In computer engineering terminology, what is meant by sampling? Include a short example and possibly a image to aid your explanation.
my description …
Pretty good!!

## Slide 68: Quiz0 review: Q6
In computer engineering terminology, what is meant by sampling? Include a short example and possibly a image to aid your explanation.
Sampling, used by computer engineers, typically refers to the process of digitizing an analogue signal, or looking at discrete instances of a continuous signal. A sample is basically a value or set of related values representing an instance in time of an analogue/real event. Usually a fixed sample period is used.
time
Analogue / real signal
sample period
a sample

## Slide 69
Image sources:
Clipart sources – public domain CC0 (http://pixabay.com/)
commons.wikimedia.org
images from flickr
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).